## Slide 1: Flight Readiness Review
University of South Alabama
Conner Denton, John Faulk, Nghia Huynh, Kent Lino, Phillip Ruschmyer, & Andrew Tindell
Mentor : Richard Kramer

## Slide 2: Final Launch Vehicle Parameters
Overall Vehicle Parameters
  Rocket height: 94 inches
  Body diameter: 4 inches
  Wall thickness: 1/16 inch
Nosecone: Ogive
Fin design: Straight Tapered

## Slide 3: Key Design Features
Hazard Detection Camera
  capable of spotting hazardous areas through point of view analysis
Turbine Energy Conversion
  on board turbine generator capable of converting energy sufficient for on board electronics

## Slide 4: Final Rocket Motor
AeroTech K1103X - 14
Total Impulse: 1789 N
Pre Burn Mass: 1459 g
Post Burn Weight:

## Slide 5: Rocket Flight Stability
Flight Stability: 2.49 cal
CP (Simulated): 73.621 inches from nose
CG (Experimental): 63.659 inches from nose

## Slide 6: Thrust to Weight Ratio
Thrust to Weight Ratio: 16.05
  Thrust: 1103 N
  Weight: 247 oz. -> 7.00 kg -> 68.69 N
Rail exit velocity:
  101 ft/s
Thrust curve of Aerotech K1103 motor.

## Slide 7: Mass Statement & Margin

## Slide 8: Recovery Parameters
Drogue Parachute Size: 12 inches
Main Parachute Size: 72 inches
Calculated Descent Rates:
  Rocket body under drogue (white): 139.44 ft/s
  Rocket body under main (pink) : 23.24 ft/s

## Slide 9: Kinetic Energy Calculations
Phases | Nosecone | Avionics Bay | Booster Bay
Take-off | 86.10 ft-lbf | 894.63 ft-lbf | 1466.39 ft-lbf
Deployment | 149.30 ft-lbf | 1551.32 ft-lbf | 2542.79 ft-lbf
Landing | 3.90 ft-lbf | 40.54 ft-lbf | 66.45 ft-lbf

## Slide 10: Predicted Drift and Altitude of Vehicle
Predicted drift from launch pad:
  5mph – 220.87 ft.
  10mph – 441.74 ft.
  15mph – 662.61 ft.
  20mph – 883.48 ft.
Predicted altitude from launch pad
  5mph – 5407 ft.
  10 mph – 5372 ft.
  15 mph – 5337 ft.
  20 mph – 5312 ft.

## Slide 11: Final Payload Design & Dimensions
Turbine Schematic
  Ground connection
  Analog input connection
Pixy Camera Schematic
  ICSP connection

## Slide 12: Final Payload Design & Dimensions
Turbine Tray
  Secured in G10 fiberglass bay
  Stationary in booster bay
Pixy Camera Tray
  Need to design Pixy Camera Tray
  Secured in G10 fiberglass bay
  Plexiglass bulkhead

## Slide 13: Payload Integration
Vehicle Attachment Scheme
Main Parachute (A): Deploy at approximately 700ft
Nosecone (B): Will deploy with main parachute
Avionics Bay (C): Houses hazard detection camera, altimeter, and parachute until apogee
Booster Bay (D): Houses shock cord, motor, and turbine generation payload
DC Wind Turbine (D): Housed in booster bay
  Turbine tray: round with spokes
  Directed air flow piping
Hazard Detection Camera (F): Located in coupler
  G10 Fiberglass Bay & Bulkhead
  Plexiglass Bulkhead

## Slide 14: Interfaces with Ground Systems
Stratologger #1: Will deploy both main designated altitude and drogue at apogee
Stratologger #2: Designated as scoring competition altimeter
PixyCam: Hazard detection payload capable of determining position away from descending vehicle
Turbine Generator: Generates and logs the amount of current produced in order to prove that it can be used it further projects to power on board electronics

## Slide 15: Payload Test Plan
Hazard Detection Pixy Camera
  Test outside in normal climate conditions
    Hinderance of weather conditions
    Effects of sunlight
  Further equation accuracy testing
    Uniquely colored tarp for color ID
    Camera coordinates
    Absolute coordinates
  Full scale testing
    Ejection from avionics bay
    Tangling with shock cord
    Tilt during descent
    Plexiglass clarity
Failsafe Drogue Deployment Turbine
  Full scale turbine voltage test with air jet
    Multimeter voltage testing
    Arduino Uno data logging
  Wind Tunnel Testing
    Airflow scoop stability
    Velocity of interior air flow
    Voltage testing
  Directed airflow piping
    Determine optimum piping positioning
    Max voltage allowance

## Slide 16: Recovery System Tests
Black Powder Charge Ejection Tests
  ~2.0 grams (unsuccessful)
  ~2.5 grams (successful)
Altimeter Tests
  Vacuum testing
  Electrical disturbances
    Aluminum tape

## Slide 17: Full Scale Flight Tests
First Full Scale Flight:
  Apogee: 3507 ft.
  Deployment: Dual with main parachute at 700 ft
  Overloaded black powder charge so both parachutes deployed at apogee
Second Full Scale Flight:
  Apogee: 2203 ft.
  Deployment: Dual with main parachute at 700
  Successful launch and recovery
Full scale test flight.

## Slide 18: Summary of Launch Vehicle Requirement Verification
Successful sub-scale launch
Safe full-scale launch
Static ground testing
OpenRocket simulations
Future parachute drag analysis

## Slide 19: Summary of Payload Requirement Verification
Sub-scale mass simulations
Full-scale mass simulations
Static ground testing
Wind tunnel testing
Drop testing of camera bay
Air jet testing of wind turbine